## Slide 1: Neuromend
By Tempest
An ICT313 Games Technology Project
Murdoch University
  Ary Bizar, Anopan Kandiah, Hannah Klinac, Alex Mlodawski, Bryan Yu

## Slide 2: Outline
Introduction
Project background
Project requirements
The solutions
Our approach
Live demonstrations
Final status
Future possibilities
Lessons learned
Questions?

## Slide 3: Project Introduction
Project Name: Neuromend
Client: Mr Shri Rai, Murdoch School of Engineering & IT
Supervisor: Dr Fairuz Shiratuddin
Tempest:
  Ary Bizar (BSc, Games Technology; BA, Games Art and Design)
    Level designer, Asset creation
  Anopan Kandiah (BSc, Computer Science, Games Technology)
    Kinect development
  Hannah Klinac (BSc, Computer Science, Games Technology)
    Leap Motion development, Project Manager
  Alex Mlodawski (BSc, Computer Science, Games Technology)
    Kinect development
  Bryan Yu (BSc, Computer Science, Games Technology)
    Razer Hydra development, Database

## Slide 4: Project Background
Stroke
  Parts of the brain may be damaged or may die
  This can result some loss of motor control,
  sensory, and cognitive abilities.
One form of rehabilitation is rewiring
Rehabilitation
  Accessibility
  Money
  Tedious/boring
  No incremental goals
  Limited
Notes: HELPING PEOPLE

## Slide 5: Project Specifications & Requirements
Specifications
  This idea of simulation rehabilitation inducing rewiring is a theory that has been shown to work elsewhere
  This project is one of the first steps toward establishing a stroke rehabilitation system
    This project involves developing the prototype platform
    Testing will be done next semester
Requirements
  Create a virtual simulation
  Design and develop 3 different tasks
  Utilize natural user interfaces devices
  Design and develop sensitivity adjustor
  Design and develop to support profiling and database
  to keep track of progress
Notes:   Project was initially created to evaluate the devices to see what could work well for a solution
  Determined that the project was useful enough to be used in a practical setting
  This project is essentially an evaluation step towards a more concrete implementation

## Slide 6: The Solutions
The main system must have:
Virtual environments
3 different tasks that require different movements
    Object Manipulation
    Obstacle Avoidance
    Way Finding
Natural user interfaces* devices (providing different accessibilities) used in conjunction with Oculus Rift (the main display)
  Keyboard and mouse* (control device)
  Razer Hydra
  Kinect
  Leap Motion
Sensitivity and other adjustable settings
  Provide incremental goals
Monitoring progress – can be assessed
Profiles on an external database

## Slide 7: Project Management
Iterative (SCRUM) methodology with weekly sprints
Weekly team/supervisor meetings
Communication
  Project room
  Facebook group
Source code control
  GitHub
Notes: Weekly team meetings: discussed requirements, issues and demonstrated progress and prototypes
*How the project was managed
*How the team was managed
Work breakdown
Work assignment

## Slide 8: Project Management - Team
Ary Bizar : Level designer, Asset creation, Mouse & keyboard development
Anopan Kandiah : Kinect development
Hannah Klinac : Leap Motion development, Project Manager
Alex Mlodawski : Kinect development
Bryan Yu : Razer Hydra development, Profiling and Database
Notes: Work breakdown
Work assignment

## Slide 9: Technologies Utilized
Main system was developed using Unity and coded using C#
Visual assets
  3DS Max
  Mudbox
  Photoshop
Database and profiling system
  MySQL
  ClearDB
Hardware
  Oculus Rift DK1
    0.4.0 SDK
  Razer Hydra
    Sixense SDK
  Kinect v1 for Windows
    V1.8 SDK
  Leap Motion
    V2 Tracking API, 2.1.5 SDK

## Slide 10: Live Demonstration Kinect – “Obstacle Avoidance”
Obstacle Avoidance Exercise
  Reactions
  Decision making
  Constant forward movement
Kinect actions
  Tracks full body
  Actions using arms and hands
  Usable by able bodied
  Adjusts heightened sensitivity

## Slide 11: Live Demonstration Razer Hydra – “Object Manipulation”
Object Manipulation Exercise
  Simple puzzle solving
  Order
  Association recognition
  Stationary user position
Razer Hydra actions
  Sixense technology
  Tracks hands
  Triggers and joysticks
  Tracks position and orientation
  Usable by able bodied
  Adjusts heightened sensitivity

## Slide 12: Live Demonstration Leap Motion – “Way Finding”
Way Finding Exercise
  Memory
  Sense of direction
  Maze hints
    Rabbits
    Jump pads
    Points of reference
Leap Motion actions
  Beta product
  Tracks hands using near infra-red frustum
  Actions using hands in the interaction area
  Tracks all 10 fingers up to 1/100th of a millimetre
  Usable by able bodied
  Adjusts heightened sensitivity

## Slide 13: Final Status
Requirements
  Virtual Simulation
  3 different tasks
  NUIs Devices
  Sensitivity adjustor
  Profiling
  Database
Playable by anyone
Interesting and enjoyable
Extensible
The project is now in a position to be extended for deployment into practical use

## Slide 14: Future Possibilities
Clinical use
  The system will be tested soon
Additional control schemes
  Speech
  Electroencephalogram (EEG)
    Records brain wave patterns
  Monitoring variables to self improve the system
    Stress
Support for future versions of the NUI devices
  Oculus Rift DK2
  Kinect 2
  Tobii EyeX (Eye Tracker)
  Leap Motion release
  Sixense Stem System (wireless motion tracking system)
  Virtuix Omni (360° treadmill)

## Slide 15: Lessons Learned
Devices
  Beta products and development kits
  Drivers clashing
  Versions/compatibility
Designing the tasks and the movements/gestures to meet requirements and to also consider the devices and what they can do
Version control and modifying joint code
Teamwork
  Decisions
  Conflict resolution
Communication is essential for success
The importance of time management
Assess and managing scope

## Slide 16: Acknowledgements
Client – Mr Shri Rai
Supervisor – Dr Fairuz Shiratuddin
Ayden-James Nolan – Music
Elly Thompson - Sounds

## Slide 17: Questions?

## Slide 18: References
http://images.sciencedaily.com/2014/08/140807163633-large.jpg
http://www.reuters.com/video/2014/03/26/virtual-reality-stroke-therapy-tricks-br?videoId=299126765
http://strokediseases.files.wordpress.com/2011/02/wpid-stroke-arm-rehabilitation.jpg
http://clearingwritersblock.com/images/brainwaves.jpg
http://www.wired.com/images_blogs/threatlevel/2012/08/eeg_headset.jpg
http://www.robotshop.com/media/files/images2/leap-motion-3d-motion-gesture-controller-10-large.jpg
http://upload.wikimedia.org/wikipedia/commons/a/ae/Oculus_Rift_-_Developer_Version_-_Front.jpg
http://me.ign.com/sm/ign_me/screenshot/w/win-a-razer-hydra-motion-controller/win-a-razer-hydra-motion-controller_2ubw.jpg
http://images.pcworld.com/images/article/2012/01/kinect-for-windows-8667082.jpg